## Slide 1
KHAYAAL
A silent guardian for elderly parents living alone — passive wellbeing monitoring, weak-signal fusion, tiered escalation.
Team Nivaan · Aditya Dubey · Rudra Pratap Singh Negi · IILM University, Greater Noida
Next.js 15 · TypeScript strict · Kotlin/Compose · ESP32 Wi-Fi CSI · Google OAuth
“Nothing to press. Nothing to wear. Nothing to remember.”

## Slide 2
THE PROBLEM
India's eldercare gap is a detection failure, not a medical one
• 149M elderly today → 347M by 2050 (41% growth per decade — fastest-ageing cohort)
• 1 in 3 falls every year past 60 · 2 in 3 of those falls injure — usually with nobody in the room
• 1 in 10 live entirely alone: 70% rural, 40% in the poorest wealth quintile
• Existing answers fail at the moment of crisis — they all require the victim to act:
  – Panic buttons: assume consciousness, orientation, reachability
  – Wearables: bought, worn daily, charged nightly — end up in a drawer
  – Cameras: surveillance inside the home → switched off
KHAYAAL · 02

## Slide 3
THE PREMISE
Absence is the signal
• “If you designed the safest possible technology for an elderly person, it wouldn't rely on them pressing anything at all.”
• Design rule that governs everything — dignity first:
  – No camera · no microphone · no message content ever read
  – No wearable · no GPS trail — home presence via Wi-Fi SSID match only
  – Child-facing UI: status + last-active + score trend. Never raw sensor data (API-enforced)
• Core inversion: the system watches for the absence of ordinary life, not the presence of danger.
KHAYAAL · 03

## Slide 4
SYSTEM ARCHITECTURE
Edge collectors → single ingest contract → fusion engine → tiered escalation
• SOURCES — Android phone: UsageStatsManager (unlock/app_use), ActivityRecognition API + accelerometer (motion), BatteryManager (charging), WifiManager SSID match (location_zone home|away)
  – OPTIONAL — ESP32-WROOM-32: Wi-Fi CSI presence (esp-csi on ESP-IDF 5.5) → presence motion|idle|lost
• TRANSPORT — one endpoint for every source: POST /api/v1/ingest {sourceId, type, value, ts} with per-source API key; USB-serial JSON bridge as fallback tunnel
• BACKEND — Next.js 15 App Router route handlers; Store interface with in-process MemoryStore (Firestore drop-in); signals retained 7 days, scored, discarded
• ENGINE — @khayaal/engine: pure, framework-free TypeScript package; deterministic advanceState() recomputes from signals + prior state
• CLIENTS — web dashboards poll state every 1.5s; Android (Kotlin 2.0, Compose) batches via WorkManager (15-min periodic + event-driven expedited flush)
KHAYAAL · 04

## Slide 5
SIGNAL SCHEMA
Signal { sourceId, type, value, ts } — normalized at the edge
• screen_event ('unlock' | 'screen_on' | 'app_open') — UsageStatsManager events
• motion (1) — accelerometer + ActivityRecognition transitions (walking / on-foot)
• charging (true | false) — ACTION_POWER_CONNECTED/DISCONNECTED + BatteryManager
• app_usage (<package>) — package name only, never content
• location_zone ('home' | 'away') — SSID match; absence of GPS permission by design
• presence ('motion' | 'idle' | 'lost') — ESP32 CSI-derived room occupancy
• manual_checkin ('ok') — the parent's one-tap I'm OK
• Absence is the primary signal: the engine scores missing ordinary life, not detected danger.
KHAYAAL · 05

## Slide 6
RISK ENGINE — @KHAYAAL/ENGINE
Rule-based weighted fusion → score 0–100 → tier bands 35 / 55 / 72
• Weighted absences (per-stream caps): morning unlock ≤30 · movement ≤28 · overnight charge 16 · room presence ≤18 · total silence ≤20 · score = clamp(Σ effect, 0, 100)
• Baseline = robust medians over a 7-day sliding window: wakeHour, chargingStartHour, dailyMotionCount — a night owl is never measured against an early riser
• location_zone 'away' scales all absence effects ×0.35 and explains, never alerts
• Confidence 0.4–1.0: unpaired ESP32 −0.15 · no charging data −0.10 · thin baseline −0.10; tier ≥ 2 gated by confidence ≥ 0.55
• Quiet hours cap escalation at tier 1 unless score ≥ 85 — a 3 AM slow night never pages the family
• Effect ramps: unlock 12 + 2 pts/20min late; motion 10 + 2 pts/30min after 6 h gap; silence 6 + 1.5 pts/30min past threshold
KHAYAAL · 06

## Slide 7
ESCALATION STATE MACHINE
advanceState() is pure — idempotent and race-safe under N concurrent pollers
• Tier 0 quiet → Tier 1 soft nudge → Tier 2 check-in prompt → Tier 3 family alert with last-known signals
• Score bands alone never escalate: dwell timers 10 / 10 / 15 min (configurable per household); exactly one step per evaluation
• Any interaction-grade signal within 5 min (unlock, app_usage, checkin, presence motion) → standdown to tier 0
• Confirmed check-in holds the ladder down 2 h (snoozeUntilTs); child ack notifies siblings; every transition appended to the events audit log
• Deterministic recompute: same signals + prior state ⇒ same state, so 1.5 s polling from web + Android cannot double-fire
• Demo time-warp: simTimeOffsetMs shifts the clock — hours compress to seconds, timers included
KHAYAAL · 07

## Slide 8
API CONTRACT — /API/V1
Versioned, typed via @khayaal/shared; consumed unchanged by web and Android
• POST /pair — {action: create | join | demo}; create links the Google account (ownerSubs)
• POST /ingest — any source; 403 on bad key; signals normalized + validated
• GET /household/{id}/state — the tick: recompute risk, advance machine, sample trend, return child-safe bundle
• POST /household/{id}/checkin · /ack · /snooze · PATCH /config (quietHours, escalationConfig, simAdvanceMinutes, learningHours)
• POST /household/{id}/demo — server-side scenario seeding (normal | slow | emergency)
• GET/POST/DELETE /household/{id}/sources — device registry; API key returned exactly once
• GET /my/households · /api/auth/google/{start,callback} · POST /api/auth/transfer (one-time phone session)
KHAYAAL · 08

## Slide 9
PRIVACY & SECURITY
Dignity is enforced by the API, not by policy
• Child bundle contains no raw signals and no API keys — the UI cannot leak what it never receives
• No camera, no microphone, no message/call content; presence via SSID match — ACCESS_FINE_LOCATION never requested
• Signals retained ~7 days, scored, discarded — no archive exists
• Per-source API keys generated once at registration; ingest re-validates on every call (403 path tested)
• Google OAuth authorization-code + OIDC profile; HMAC-SHA256 signed HttpOnly SameSite session cookies (30 d)
• Phone inherits sessions via one-time 5-minute transfer links — Google's IP-URI ban never touches the device
KHAYAAL · 09

## Slide 10
ANDROID CLIENT — PHASE 2, SHIPPED
Kotlin 2.0 · Jetpack Compose · Material3 · MVVM · WorkManager
• Pairing: 6-digit code → POST /pair join → POST sources → DataStore (householdId, sourceId, apiKey, base URL)
• SignalRecorder: in-memory + DataStore-snapshot queue, mutex-guarded, one POST per signal; 403 clears queue, 5xx/IOException → Result.retry()
• Collectors: USER_PRESENT, POWER_CONNECTED/DISCONNECTED, ActivityRecognition transitions (5 min), significant-motion trigger fallback (permission-free), SSID-match presence
• Doze-aware scheduling: 15-min periodic ingest, 10-min state poll, expedited unlock flush
• Notification channels: khayaal-care (DEFAULT, tiers 1–2, tier-1 silent) · khayaal-urgent (HIGH, tier 3, full-screen intent) with I'm OK / Snooze actions; notifies only on tier rises
• kotlinx.serialization DTOs (ignoreUnknownKeys) mirror the wire shapes incl. polymorphic signal values
KHAYAAL · 10

## Slide 11
ESP32 ROOM SENSOR
Wi-Fi CSI presence sensing — no camera, no wearable, nothing worn
• ESP32-WROOM-32 · PlatformIO · Arduino core 3.3 on ESP-IDF 5.5; CSI amplitude variance over rolling 100 AP frames, BSSID-filtered
• State machine: variance > threshold for 2 s → motion · quiet 10 min → idle · Wi-Fi down → lost · 30 s heartbeats
• Calibration: serial 'cal' command logs variance 60 s and suggests ~2× idle-p95; config persisted in NVS
• Dual transport: LAN HTTPClient (5 s timeout, 1→60 s backoff) or serial JSON lines consumed by the Python bridge → same /api/v1/ingest
• Privacy: only the presence scalar leaves the device — never raw CSI
• Validated end-to-end: bridge forwarded idle/motion/idle/lost → 200 ok; wrong key → 403
KHAYAAL · 11

## Slide 12
VERIFICATION
16 unit tests · CI green · end-to-end proven
• Engine fixtures: normal day, late wake, no movement 6 h, phone dead, parent away, presence lost, quiet-hours cap, dwell timers, idempotency, learning window, baseline learning — 16/16 passing
• CI (GitHub Actions): typecheck shared+engine → engine tests → next build → Android assembleDebug → APK artifact on every push
• End-to-end Android: emulator pairing — join 200 → source registration 200 → state polling 200 → home screen live
• Escalation demo: seeded emergency scores 96 → ladder walks 1 → 2 → 3 under simulated clock, fully audited in events
• Instant demo mode: onboarding seeds a declared prior + one day of history — full confidence, real score from the first request
KHAYAAL · 12

## Slide 13
ROADMAP
From working prototype to pilot
• Firestore adapter — Store interface already defined; transactional setState for multi-instance safety
• FCM push — needs a Firebase project; in-app + polling cover the demo today
• ML phase 2: per-user Isolation Forest / LSTM behind the same engine interface, TensorFlow Lite on-device
• Pilot questions this deck answers honestly: Wi-Fi CSI reliability across room layouts · false-alarm rate of the baseline model in real households
• ESP32 flash path ready: erase-flash → upload → monitor (3 commands) after a physical replug
KHAYAAL · 13

## Slide 14
Technology protects an elderly person only when it asks nothing of them.
KHAYAAL · Team Nivaan · Aditya Dubey · Rudra Pratap Singh Negi
github.com/theguysudo/Khyaal · hello@khayaal.care